# Solutions gas turbine theory - MTF171

Exam. 2003-06-03

Problem 1:

Assume polytropic efficiencies of 88% on compressor and turbine.  Since the turbine operates uncooled a realistic value on a conventionally cast turbine is 1200 K.

ISA standard => t1 = 288.15, p1 = 101.325 kPa. Compressor exit station:

t2 = 566.01, p2 = 810.6 kPa

Assume a pressure loss value of 3%, which gives p3 = 786.3 kPa, t3 = 1200 K.  The turbine exit station obtained from:

t4 = 764.8 K, p4 = p1= ambient pressure. The power output is

Power requirement per engine is 17.90 MW which gives a required mass flow per engine of about

m = 82.28 kg/s.

Problem 2:

Interpolation in compressor map at the n=150*0.922=138.9 rps rotational speed line, and calculating the corrected compressor mass flow gives (pressure in bars):

| m | m*sqrt(T01)/P01 | rc | etac |
| --- | --- | --- | --- |
| 64.5000 | 1080.6 | 4.4750 | 0.8125 |
| 70.4250 | 1179.8 | 4.0800 | 0.8462 |
| 75.6000 | 1266.5 | 3.2900 | 0.8000 |

The x-function can be used to determine the corrected turbine massflow (pressure in bars and M=1):

which directly yields the turbine inlet temperature at the three selected off-design points.

| m*sqrt(T03)/P03 | t03 (K) |
| --- | --- |
| 516.56 | 1318.7 |
| 516.56 | 919.5 |
| 516.56 | 518.8 |

The power output from the load turbine is then determined by (neglecting mechanical efficiency):

where the temperature drops are obtained from:

using the relation:

and

the powers and temperature drops are:

| tdeltc | tdeltt | power (MW) | 2*power (MW) |
| --- | --- | --- | --- |
| 189.5258 | 366.5463 | 14.856 | 29.712 |
| 168.3531 | 242.1127 | 7.659 | 15.318 |
| 145.9854 | 118.3135 | negative | negative |

Inserting the result in the propeller map (double the gas turbine powers) shows that the first point is very close to the propeller power at that speed. Thus the match point is approximately that of the first selected point which is close to surge. This is in agreement with the experiences of the russians. A bleed valve in the rear stages, variable geometry or modifications to the turbine area (increasing), may be used to overcome this difficulty. The engine is likely to have been started with any or all of these relieving schemes. The problem would most likely be solved if these schemes were used also at such high rotational speed. This would, however, reduce the performance of the engine.

Problem 3:

Cooling reduces efficiency but increases specific power output.

To maximize the output power one should minimize the power requirement by the compressors.

t4  is obtained from the isentropic relations

which gives (T3=T1)