## Slide 1: FSI for Assessing Nerve Injury During Whiplash Motion
Hua-Dong Yao, Håkan Nilsson, Mats Svensson
Department of Applied Mechanics,
Chalmers University of Technology, Sweden
2013-11-13

## Slide 2: List
Background
Methodology
Computational Settings
Results
Summary

## Slide 3
The injuries happen in rear-end car crashes.
Introduction to Whiplash
Damage at
  Intervertebral joints,
  Vertebral discs,
  Ligaments,
  Cervical muscles
  Nerve roots.
Our concern

## Slide 4
Damage occurs at ganglion of spinal nerve.
Highly impulsive pressure is observed in venous plexus embedded in spinal canal.
Ganglion damage is possibly relative to this impulsive pressure.
Nerve Injury during Whiplash Motion
Giancarlo Canavese and Mats Svensson, Chalmers, 2004
Ganglion
Venous plexus

## Slide 5
The system is solved using the strongly coupled partitioned method.
FSI solver of OpenFOAM
Giancarlo Canavese and Mats Svensson, Chalmers, 2004

## Slide 6
Strongly Coupled Partitioned Method
Solve mesh
Interface velocity
Solve flow
Interface load
Solve structure
Interface deformation
Step i-1
Step i
Check Residual
No
Yes

## Slide 7
The Aitken relaxation applies to accelerate iterations.
Acceleration Scheme

## Slide 8
Fluid is incompressible.
Fluid solver utilizes the PISO algorithm.
Structure has linear elasticity.
Structure solver employs the discretization of a second-order finite volume method in space and a second-order backward method in time.
Fluid and Structure Solvers
Governing equation of structure
Discretization in space
Discretization in time

## Slide 9
Simplified Geometry
Solid part
Fluid part
Ganglion
Dura mater
Computational geometry is simplified
based on the human anatomy.
The geometry is two-dimensional.
31.3 mm
24.5 mm
3.9 mm
5.4 mm

## Slide 10
The mesh is unstructured.
ICEM is used for mesh generation.
Height of the first layer of the fluid mesh is 0.01 mm.
Mesh Generation

## Slide 11
Boundary Conditions
wall
wall
symmetryPlane
wall
pressure: fixedValue
velocity: zeroGradient
pressure: timeVaryingUniformFixedValue
velocity: zeroGradient
1D modeling with Simulink

## Slide 12
Computation Condition
Parallel computation with four processors.
Decomposition of the computational domain adopts the method of ‘simple’.
Time interval – Δt -- is 5e-6 sec.
Simulated physical period is 0.2 sec.
Wall-clock time is approximately 36 sec per step.
Pressure at the inlet

## Slide 13
Results
Movie

## Slide 14
Deformation of the ganglion is associated with pressure variation.
Results
Pressure at the inlet

## Slide 15: Summary
The FSI solver of OpenFOAM succeeds in predicting the nerve injury of whiplash.
The computation is paralleled.
The ganglion deformation is connected with the pressure impulsion of venous plexus, which is reproduced by imposing a varying pressure boundary condition at the inlet.
We will extend the present 2D simulation to 3D.

## Slide 16: Thanks!

## Slide 17
Results
Giancarlo Canavese and Mats Svensson, Chalmers, 2004
Modelling by Simulink
Experiment
FSI by OpenFOAM

## Slide 18
The injury
Computation Setting -- Simplified Geometry