## Slide 1: surfaceFilmModel extensions in an industrial setting
Johan Nilsson Gothenburg, Sweden
2017-11-15

## Slide 2: Creo Dynamics – A New Way of Working
The synergy between our three business areas helps us maintain state-of-the-art knowledge, so that we can provide our customers with the very best specialist technical services.
Consulting
Research
Innovation
Providing state-of-the-art specialist consulting services
Participation in 7 research projects (Sweden & EU)
Documented history of delivering innovation, giving customers a competitive edge

## Slide 3: Creo Dynamics – Competence Areas
Fluid Mechanics / CFD
Acoustics
Pioneering in Active Noise Control systems for aerospace & automotive applications
Keep informative sound, attenuate irritating sound & amplify impressive sound
Solving flow problems using CFD or analytical methods
External flow, internal flow, heat transfer, combustion etc.
Open source CFD methodology, leveraging our Formula One experience for leading performance & cost efficiency
Building intelligence into composite structures
Health monitoring, load/temperature sensing, efficient NDT methods
Analysis & optimization of lightweight structures
Smart Structures

## Slide 4: Problem description – Machine sterilisation using hydrogen peroxide
Tetra Pak filling machine sterilization, i.e. sterilization of the machine, not the product nor the package material
Gaseous hydrogen peroxide (H2O2) is used to kill bacteria
The hydrogen peroxide condensates inside the filling machine
At the end of the sterilization process, all hydrogen peroxide should be evaporated
Notes: This project has been carried out for Tetra Pak. Tetra Pak is a large multinational food packaging company which has been particularly successful with its aseptic package systems. The idea with an aseptic package is that if you have a completely sterile process you can get a product with a long shelf time without the need of refrigeration. Obviously you need a sterile product and container, but it’s also important that the entire process including the filling machine itself is sterile.

## Slide 5: Problem description – Machine sterilisation using hydrogen peroxide
Pipe – solid – cold
Air + H2O2 + H2O – gas – hot
Flow
Phase 0: Initial condition

## Slide 6: Problem description – Machine sterilisation using hydrogen peroxide
Pipe – solid – cold
Air + H2O2 + H2O – gas – hot
Flow
Film – liquid – H2O2 + H2O
Phase 1: H2O2 and H2O condensate on the pipe forming a liquid film

## Slide 7: Problem description – Machine sterilisation using hydrogen peroxide
Pipe – solid – warm
Air – gas – hot
Flow
Film – liquid – H2O2 + H2O
Phase 2: Dry air is sent into the machine, no H2O2 and H2O. The film begins to evaporate.

## Slide 8: Problem description – Machine sterilisation using hydrogen peroxide
Pipe – solid – warmer
Air – gas – hot
Flow
Film – liquid – H2O2 + H2O
Phase 3: Since H2O evaporates faster than H2O2, the H2O2 concentration increase in the film.

## Slide 9: Problem description – Machine sterilisation using hydrogen peroxide
Pipe – solid – hot
Air – gas – hot
Flow
Phase 4: The liquid film has evaporated completely

## Slide 10: Challenges involved
A lot of physics going on:
Conjugate heat transfer simulation necessary for proper heat transfer
Surface film modelling needed
Film requirements
  Two component
  Phase change (evaporation and condensation)
  Moving/flowing film
  Heat transfer
  Separation from stripping etc
  Injection from droplets
Gas domain needs to be multi-component
Spray and droplets

## Slide 11: Stock OpenFOAM capabilities – solvers
reactingParcelFilmFoam and chtMultiRegionFoam
reactingParcelFilmFoam
  Uses surfaceFilmModel for surface film modelling
  Multiple components in the gas domain
  Spray and droplets
  Lacks CHT (Conjugate Heat Transfer) coupling with other domains except for the film
chtMultiRegionFoam
  Multi-region conjugate heat transfer coupling
  Single component
  No spray or droplets support
Solution: Add surfaceFilmModel, multi-components and spray/droplet support from reactingParcelFilmFoam into chtMultiRegionFoam to create chtMultiRegionFilmFoam

## Slide 12: Stock OpenFOAM capabilities – surfaceFilmModel
Uses ”thin-film” assumptions
  Wall-normal velocity is zero
  Wall-tangential diffusion (momentum, energy) negligible compared to wall-normal diffusion
This means that the transport equations can be integrated in the wall-normal direction
Solves film continuity, momentum, energy and thickness equations
Lives in its own region (domain)
Mesh is extruded from gas or solid domain and is one cell thick
Film thickness is unrelated to the cell thickness in the film domain
film
fluid

## Slide 13: Features that needed to be added or improved to the film library
Missing features that needed to be added
  Two-component film
Features that needed improvement
  Coupling to solid region
  Gas to film momentum coupling
  Heat transfer film-gas and film-solid
  Phase change models

## Slide 14: Two component film
Specie transport equation added
The thermodynamical properties are calculated using the built-in liquidMixtureProperties class
  Density, saturation pressure, latent heat and specific heat capacity is computed as the mass fraction weighted average
  The surface tension force is based on the surface mole fractions estimated from Raoult’s law
  Thermal conductivity is estimated using Li’s method
  The vapour diffusivity is calculated using Blanc’s law

## Slide 15: Heat transfer
CHT type heat transfer needed
Exisiting connectivity between film and gas regions
Added film and solid region connectivity
film
gas
solid

## Slide 16: Heat transfer – stock OpenFOAM
is the heat transfer coefficient
The above enters as a source term into the film heat equation
Two models exists for , constant and mapped.
  constantHeatTransfer – is a specified constant over the entire patch
  mappedConvectiveHeatTransfer – is mapped from a field that is registred to the gas domain. There it is computed based on a Nusselt number correlation:
  is the thermal conductivity of the film liquid
  is a user specified characteristic length

## Slide 17: Heat transfer – present work
Use local heat balances instead of global!
Begin from the Fourier’s law
This gives
is the film thickness
A new temperature BC for use in gas, film and solid domains is also implemented
Existing turbulentTemperatureCoupledBaffleMixed is extended so that it handles that some part of the film domain are covered in a liquid film and some are dry

## Slide 18: Two component phase change
Stock OpenFOAM surfaceFilmModel only supports evaporation and boiling
The stock evaporation model is based on a Sherwood number relation that is analogous to the Nusselt number relation for the heat transfer coefficient
The stock evaporation model requires a characteristic length to be specified
In the present work we implement Raoult’s law that is based on partial pressures
Basically, evaporation or condensation takes place if the specie concentration immediately above the film is higher or lower than in the nearest gas cell center.

## Slide 19: Momentum coupling
Stock OpenFOAM uses a simplified model for the momentum coupling
The shear stress in the film on the surface against the gas domain is stock OpenFOAM:
is a user specified friction coefficient
In the present work we instead use that the shear stress should be equal on both sides of the film-gas interface
Once again, base the implementation on local balances instead of global coefficients

## Slide 20: Simulations
Only parts of the supply system is simulated in this work – the end goal was to simulate a much larger part of the machine
URANS simulation
Mesh size is 770 kCells
Simulated time is 42 s
Animation

## Slide 21: Concluding remarks
The stock surfaceFilmModel has been extended and improved to suit the needs of Tetra Pak
A new solver, chtMultiRegionFilmFoam has been created for use with the new film model

## Slide 22: Stock OpenFOAM capabilities – Exisiting features
Contact angle forces
Thermocapillary forces
Radiation support
Curvature separation
Dripping injection
Impingement
Capillary pressure
Gas-phase pressure
Gravity force